## Slide 1: Near-surface characterization and S-wave statics: Bradford 3D-3C seismic survey (Marcellus shale)
AGL Annual Meeting, Houston, TX
16th May, 2013
Soumya Roy
Advisor: Dr. Robert R. Stewart
Daniel A. Russell (1999)

## Slide 2
Motivation and objective
- Near-surface characterization
S-wave velocities (from surface-wave inversion)
- La Marque, TX - YBRA field camp, MO
- Meteor crater, AZ
Limitations and developments
  - Lateral heterogeneity - Full-waveform inversion
Overview
Bradford survey, Pennsylvania (Data courtesy: GeoKinetics)
- 3D-3C seismic survey - S-wave statics
Summary

## Slide 3
To provide near-surface solution for multicomponent seismic analysis
To develop a non-invasive, inexpensive, and fast method to estimate 2D (and 3D) shallow-subsurface material properties
S-wave velocities from surface-wave inversion
- To identify shallow geological structures
- To correct for time delays in seismic waves (statics)
- To predict densities
- Full-waveform inversion (FWI)
Motivation And Objective

## Slide 4
Survey Locations
0
788
Km
Hockley
La Marque
Meteor Crater
YBRA Field Camp
Bradford
Meteor Crater
0
788
Km
1. La Marque, TX
4. Bradford, PA
3. Meteor Crater, AZ
2. YBRA Field Camp, MT

## Slide 5
Surface-wave Inversion: MASW
Multichannel Analysis of Surface Waves (MASW)
(Park et al., 1998; ibid 1999; Xia et al., 1999)
Seismic Data: La Marque, TX
Offset (m)
t (ms)
0
94
0
1000
Fundamental Modes
Higher Modes
Frequency (Hz)
Phase velocity (m/s)
700
500
100
300
10
20
30
40
Dispersion Curve
…
…
S1
Sn
0
100
Amplitude (%)

## Slide 6
S-wave Velocities: La Marque
44
46
48
50
52
Depth (m)
5
10
15
20
Distance (m)
100
200
300
400
S-wave Velocity (m/s)
UH
La Marque, TX
Source interval: 2 m
Receiver interval: 2 m

## Slide 7
S-wave Velocities: YBRA
YBRA
Wyoming
Idaho
Montana
Source interval: 3 m
Receiver interval: 3 m

## Slide 8
Barringer (Meteor) Crater, Arizona
272
0
m
Bowl-shaped depression
Crater rim

## Slide 9
S-wave Velocities: Meteor Crater
Roy, S. and R. R. Stewart, 2012, Near-surface seismic investigation of Barringer (Meteor) Crater, Arizona, Journal of
Environmental and Engineering Geophysics, 17, 117-127
Source interval: 3 m
Receiver interval: 3 m

## Slide 10
Bradford 3D-3C Seismic Survey
Source: Dynamite
Receiver Interval: 110 ft
Data courtesy: GeoKinetics
(0 ft)
(10450 ft)

## Slide 11
Chart: 
Statics: Bradford Survey
NW
Distance (ft)
0
2200
4400
6600
8800
P-wave statics
S-wave statics
Statics (ms)

## Slide 12
S-wave Velocity: Bradford
zw

## Slide 13
Total S-wave Receiver Statics
Distance (ft)
0
2200
4400
6600
8800

## Slide 14
Smooth S-wave LVL Statics
Lack of in-line shots: 2D vs. 3D geometry
Selection of long receiver-spread range
Smooth S-wave statics can be applied at early processing stage
From MASW
From GeoKinetics
(Smoothed)
Total statics – Elevation statics
Meteor Crater S-wave LVL statics
40
60
80
50
70
90
Distance (m)
S-wave LVL statics (ms)
36
312
609

## Slide 15
Lateral Heterogeneity and MASW
Gentle lateral variation

## Slide 16
Compare modeled and
observed data trace by trace
Future Scope: Elastic FWI
VP from refraction analysis
VS from MASW
ρ from well log or predicted
from VP and VS
Initial model
Forward Modeling
(ANIVEC; Manning, 2007)
Inversion and Update model
VP1,QP1,VS1,QS1,ρ1,T1
VP2,QP2,VS2,QS2,ρ2,T2
VPn,QPn,VSn,QSn,ρn
Time (ms)
Offset (m)
Modeled data
Time (ms)
Offset (m)
Observed data
MATLAB
Q : Attenuation
T : Thickness

## Slide 17
Lateral Heterogeneity (Physical Modeling)

## Slide 18
Numerical Modeling (Manning, 2007)
Medium 1 (Plexiglas)
Medium 2 (Aluminum)
VP = 2740 m/s
VS = 1380 m/s
VP = 6300 m/s
VS = 3100 m/s
Fault
Lateral Heterogeneity (Numerical Modeling)
Distance (m)
120
400
616
Time (ms)
0
100
200
300
400
500
600
Fault
Back-propagated
ground roll

## Slide 19
Basic FWI: Lateral Heterogeneity
Time (ms)
0
200
400
600
Observed
Modeled
Far offset trace

## Slide 20
Basic FWI: Lateral Heterogeneity
Distance (m)
Time (ms)
Fault
0
100
200
300
400
500
600
120
400
616
Actual VS1 : 1380 m/s
Actual VS2 : 3100 m/s
From MASW
Input VS1: 1280 m/s
Input VS2 : 2900 m/s
After FWI
Final VS1: 1380.04 m/s
Final VS2 : 3101 m/s
Observed ~ Modeled

## Slide 21
Summary
Near-surface VS values may be very low and variable
VS from MASW provides smooth velocity model
P- and S-wave statics are different
S-wave statics from MASW – a standalone method
Lateral heterogeneity may affect MASW method
FWI - a future step to handle lateral heterogeneity
Distance
Depth

## Slide 22
Acknowledgments
Dr. Robert R. Stewart
Mr. Bode Omoboya, Mr. Li Chang, and Mr. Eray Kocel
Dr. Nikolay Dyaur
My friends and colleagues at AGL
GeoKinetics: Mr. Suat Altan
www.agl.uh.edu
Thank You…
Meteor Crater Field Crew (May, 2010)

## Slide 24
Methodology: MASW
Multichannel Analysis of Surface Waves (MASW)
- Generation of dispersion curves (phase velocity versus frequency plots)
(Park et al., 1998; ibid 1999; Xia et al., 1999)
x
t
x
f
Amplitude spectra
Phase

## Slide 25
MASW (Dispersion curves)
Values are stacked over entire offset
The maximum value is obtained when -
x
t
x
f
Phase spectra
*
, ω = angular frequency and cω = phase velocity

## Slide 26
Reflector
Unconsolidated
sediments
Base of
low-velocity
layer (LVL)
Earth surface
Consolidated
sediments
3C Receiver
Radial
Transverse
Vertical
Source
P-wave
S-wave
Zw
P-wave
S-wave
Statics Calculation
Base of low-velocity layer (LVL)
(Cox, 1999)

## Slide 27
Surface-wave Inversion (MASW)
MASW: Multichannel Analysis of Surface Waves
- Park et al., 1998; Xia et al., 1999
Dispersion curve for one shot gather

## Slide 28
Bradford: Marcellus Shale Case

## Slide 29
Basic FWI: Lateral Heterogeneity
Time (ms)
0
200
400
600
Observed
Modeled
Near offset trace