## Slide 1: Locating microseismic events:
Omer Akbas Department of Atmospheric and Earth Sciences University of Houston 16 May 2013 Thursday
A Physical Modeling Comparison Using P and S waves in Surface and Borehole Data

## Slide 2: Questions to address
How the algorithm works?
Can S-waves be helpful besides P-waves?
How borehole receivers affect location uncertainty?
Can amplitude be used apart from traveltimes?
How do multi-component receivers help us locate events?
Can we make it run faster with parallel computing?

## Slide 3: Microseismicity tells us about the induced fractures...
Location
Length
Height
Growth
Fractures
Complexity
Orientation

## Slide 4
307.70 mm
93.9 mm
242.45 mm
50.7 mm
Physical Modeling – Data Acquisition

## Slide 6: Velocity Measurements
 | P-Wave Velocity (m/s) | S-Wave Velocity (m/s)
Plexiglas | 2720 | 1382
Aluminum | 6451 | 3108

## Slide 7: Location Algorithm: How it works?
Locating events
Traveltime residual
Amplitudes
Amplitude/Traveltime Ratio

## Slide 8
Locating Events: via traveltimes

## Slide 9
3D View of the Model

## Slide 10
Create a grid area
Dense grid interval –» More accurate but slow
Coarse grid interval –» Less accurate but faster
To achieve fast and accurate solution:
collapsing grid algorithm is implemented.

## Slide 11
Step 1: Create grid area with coarse spacing
Search starts with coarse grid spacing (200 meters)

## Slide 12
Step 2: Calculate synthetic traveltimes
Traveltimes are calculated via ray tracing for each potential source location

## Slide 13
Step 3: Compute the traveltime residuals
Approximate source location is found with a coarse grid spacing

## Slide 14
Step 4: Create another grid area with dense grid spacing

## Slide 15
Step 5: Pick the location minimizes the traveltime residual
Source coordinates are located after second iteration
Corresponds to area of source transducer

## Slide 16: Locating Events: via amplitudes

## Slide 17
Generating Stacked Energy Contour Map
For each potential source location, we have:
(X-Y-Z) coordinates
A stacked amplitude value
Total Traveltime:
0.044 ms

## Slide 18
Stacked Energy Contour Map

## Slide 19: Slice at Z=1450 meters
Higher amplitude values are more likely to be the source location

## Slide 20
Amplitude/Traveltime ratio contour map

## Slide 21: Slice at Z=1450 meters
The Apex of the ratio corresponds to source location

## Slide 22: More Experiments Results
Approach | Coordinates (X,Y,Z) | RMS Error
Actual Source Position | 2160, 1200,1450 | -
P-wave & All Receivers | 2190, 1170,1450 | 0.17µs
P-wave & Excluding downhole | 2120, 1240,1450 | 0.31µs
S-wave & All Receivers | 2240, 1260,1430 | 1.14µs
S-wave & Excluding downhole | 2090, 1280,1410 | 1.32µs

## Slide 23: Comparison of the results

## Slide 24
Optimizing the Algorithm
CPU : AMD Phenom X6 1055T @3.3 GHz
GPU: NVidia GeForce GTX 460 1GB; @850 MHz
RAM: 8 GB RAM @1600MHz,

## Slide 25: Conclusion
How the algorithm works?
  It is based on grid searching technique; also it uses collapsing grid algorithm.
Can amplitude be used apart from traveltime residuals?
  Yes, amplitude can be used to locate events. Amplitude/traveltime ratio is less noisy.
Can S-waves be helpful besides P-waves?
  Yes, we are able to locate events with using only S-waves.
How borehole receivers affect location uncertainty?
  Excluding well-side receivers increases RMS error.
Any help of using 3-C receivers?
  Allows us to compute polarization of P and S-waves.
Can we make it run faster with parallel computing?
  Yes, we can. Significant increase in performance is observed with GPU computing.

## Slide 26: Future Works
More complex physical models will be tested.
Numerical dataset will be generated by using elastic finite-difference method to test the algorithm.
Polarization information can be used in a way to locate events.
Focal mechanism and radiation pattern determination.

## Slide 27: Acknowledgements
Dr. Robert Stewart
Dr. Nikolay Dyaur
Allied Geophysical Laboratories

## Slide 28
END OF THE SLIDES
Thanks for your attention

## Slide 29
X-Z View of the Model
MapView of the Model

## Slide 30
Generating Stacked Energy Contour Map
Total Traveltime:
0.044 ms
0.044 ms

## Slide 31: Radiation Patterns