## Slide 1
Near-Surface Geophysical Investigation of the 2010 Haiti Earthquake Epicentral Area
Eray Kocel, Robert R. Stewart, Paul Mann, and Li Chang
AGL Research Update, University of Houston
April 2014

## Slide 2
Introduction
      2010, Haiti Earthquake with 200,000 death
      No surface expression
      Recent studies suggesting the existence of a blind fault
Selection of Survey Location
            Léogâne fan= Epicentral area
            No prior on-land seismic reflection data
Geophysical data
      Density and Ultrasonic Lab. Measurements
      Seismic Data
          P-wave Refraction
          Shear-wave via MASW
          Shear-wave refraction
          P-wave reflection
      Gravity Data
Integrated Near-Surface Results
      What we have learned so far
Outline

## Slide 3
We are only 900 miles away from a major plate boundary
Houston
Hispaniola
North American Plate
Caribbean Plate
Haiti

## Slide 4
Haiti Project
Characterize and analyze the subsurface structure
Measure near-surface sediment properties
(3) Attempt to find and understand the blind faults that may have given rise to the 2010 earthquake
(4) Better understanding the local geology
Objective
January 12, 2010, 7.0 magnitude.
Known: Major strike slip fault,
Enriquillo Plantain Garden Fault Zone.
Hypothesis: Unrecognized, neighboring fault (Léogâne)
2010 Earthquake epicenter

## Slide 5
Why Léogâne?
Recent studies concentrated at this area
  Interferogram and Aftershock studies
  Uplift studies
  Aerial and Satellite images
  Seismicity studies
Enriquillo fault is dipping towards south
Léogâne fault is dipping towards North
Survey Locations
Calais et al, 2010
Hayes et al, 2010

## Slide 6
Laboratory Measurements
No outcrop in the area, only fan sediments
Sample A and C collected 20km away
Sample B is collected 5km away
Survey location; Just south of EPGFZ
ρ= Vp0.25
= 0.31, Vp= 2250 m
Gardner’s relationship
ρ estimated = 2.13 g/cc
ρ measured= 2.01 g/cc
Sample B

## Slide 7
Léogâne Surveys
Sources:
2012- Hammer Source 4.5 kg
2013-Accelerated Weight Drop 45 kg
2014- Vibroseis

## Slide 8
P-wave Refraction Studies
Analysis completed on 2 seismic lines (Line A and Line B) for a 80 m deep model
(1)Top layers are thicker towards south
(2)Low P-wave velocities for top 40 to 50 m
(3)Relatively consolidated layer boundary is located between 40 to 50m
Line A
Line B

## Slide 9
Shear wave studies
Shear wave velocities obtained by MASW method
Line D
Line B
Low S-wave velocities for 20 m deep model
Line A- top layer shows slight thickening towards south
Overlapping lines (B and D)
Velocity inversion on line B and D observed
Line A

## Slide 10
P-wave Reflection Studies
Line A
Line B
Overall low velocities observed
Top-low velocity layer thickens towards South
Abruptions and discontinuities observed
Strong reflection around 60-80 ms
Time migrated images revealed up to 500 ms (roughly 350 m)

## Slide 11
Gravity Analysis
Top sediment density obtained from lab. measurements and Gardner’s estimation, 2.0 g/cc
The bedrock the density is 2.7 g / cc
No prior well or seismic data
Thinning of layers towards North.
Localized gravity anomalies interpreted as the affects of faulting

## Slide 12
Lab. Measurements with Seismic: Limestone vs unconsolidated sed. Boundary around 50 m
Refraction seismic: (1)Thickening low velocity layers towards South, (2)Boundary at 50m
Known: (1)EPGF dipping south, (2)survey location
Gravity surveys: Thinning of fan sediments towards North
Integrated Near-Surface Results
Reflection seismic: (1)Channel bodies, (2)Some minor faults
depth
distance
Subsurface Layers
>2250 m/s
<2250 m/s
Relatively consolidated limestone unit

## Slide 13
              Future plans
2014 surveys with stronger seismic source
Imaging target up to 1-2 km
Full deployment of nodes (donations from Geospace)
Future Plans
                Completed
2012 and 2013 surveys were completed
Near-surface analysis provided useful geotechnical information
First on-land reflection seismic data
Tested node systems

## Slide 14
Geoscientists Without Borders
Allied Geophysical Laboratories
Anoop William
Haiti Bureau of Mines and Energy employees
Gedco-processing software
Acknowledgements

## Slide 15
THANK YOU

## Slide 18
50
Depth (m)
350
0
50
Depth (m)
350
0

## Slide 19
Houston
Hispaniola
North American Plate
Caribbean Plate

## Slide 20
Future Work
depth
distance
Subsurface Layers

## Slide 21
Integrated Near-Surface Results
Laboratory Measurements:
        Densities and velocities are calculated
        Sample B identified as a layered limestone
        Sample B has velocity range of 2.35 to 2.92 km/sec, and density of 2.01 g/cc
        Gardner relationship (using Vp from refraction analysis) estimated the density 2.13 g/cc
Seismic Data
  Refraction Data
  Reflection Data
  Shear Data
Gravity
Laboratory Measurements
Seismic Data
  Refraction Data:
        Velocities between 500 m/s and 2250 m/s for 80 m deep model
        Slight thickening of low velocity layers towards south (EPGFZ)
        Top 40-50 m of the subsurface is highly saturated and seismically weak sedimentary layer
        Deeper velocities are similar to the measured velocity of Sample B(Limestone)
  Reflection Data
  Shear Data
Gravity
Laboratory Measurements
Seismic Data
  Refraction Data
  Reflection Data:
    Vertical-cable lines were able to image up to 500 ms, roughly 350m
    On all seismic sections, some disruptions at the subsurface layers and discontinuities were seen within the first 200 ms of data, which suggests a complicated shallow subsurface geology
    We identified discontinuous layers as 20-50-m thick channel bodies deposited on previous fan surfaces
    Strong reflections observed around 80-100 ms, which corresponds to velocity contrast around 40-50 m. on refraction models.
    The contrast may be due to transition from weak, seismically slow layers to relatively more compacted limestone layers (refraction velocities are in the order of lab. measurements for sample B)
  Shear Data
Gravity
Laboratory Measurements
Seismic Data
  Refraction Data:
  Reflection Data
  Shear Data:
        The results obtained from MASW studies indicate ranging velocities of 130-200 m/s for shear wave
        The inversion of high velocity layers interpretetd as the channel bodies. Coarse .... can have relatively higher velocities
        On a similar tectonic region (San Francisco, California), these velocity values suggests that the near surface soil at Léogâne fan is ‘’Class E’’ or unconsolidated and highly saturated sediments. We believe that the unconsolidated, soft, seismically slow soil is the reason for the devastation at the nearest city (Léogâne)
Gravity
Laboratory Measurements
Seismic Data
  Refraction Data:
  Reflection Data
  Shear Data
Gravity Data:
    Due to limited spread of the gravity line over the Léogâne fan (roughly 3 km). Depth of investigation is around 1.5 km (half of the offset, at best), which should mainly reflect the change over the fan thickness
    Gravity readings are decreasing towards north (away from the main fault, due to thinning of the fan). Localized variations of the gravity readings are interpreted as the affects of faulting

## Slide 22
P-wave Reflection Studies

## Slide 23
Time (ms)
Distance (m)
0
250
850
500
250
100
200
140 m/s
110 m/s
260 m/s
245 m/s

## Slide 24
Shear wave studies