## Slide 1
Fractional Matching Pursuit Decomposition (FMPD)
Mingyong Chen
May 2nd 2012
Advisor: John P. Castagna
Notes: After this two-year study in UH, I finally know how to establish my understanding in this field, exploration geophysics. In fact, I got some points in my mind that I am willing to share. I will be more than appreciated to know from you after this presentation that my understanding was wrong. Cause in that case, my effort in defending my argument would certainly push me up to getting close to your level, which is high up to the ceiling. Oh no, much higher.

## Slide 2
Background---STFT, CWT and MPD
Fractional Matching Pursuit Decomposition
Computational Simulation
Results: MPD versus FMPD
Conclusion
Contents

## Slide 3
Background---STFT, CWT and MPD
Fractional Matching Pursuit Decomposition
Computational Simulation
Results: MPD versus FMPD
Conclusion
Contents

## Slide 4
Localized information is valuable
Fourier Transform: information of stationary signals
Seismic Signals: NON-STATIONARY
Stationary Signal: constant statistical parameters over time
Short Time Fourier Transform(STFT): Primary solution
The need for Time freq analysis
Notes: Wigner Rahaczek Page

## Slide 5
Short time Fourier Transform(STFT)
Break into segments
Applied FT on each segment
Lay out the spectrum along time
Display all the spectra
Assumption: truncated signals are stationary
Con: window determine combined resolution
Notes: AssumptionThe truncated signal is considered stationary if the window is small enough.
Con: the resolution is fixed once the window is chosen.
The formula of Fourier transform with a window.
The multiplication in time domain is the convolution in spectral domain. Therefore, the spectrum is modified by the window. The major information is still preserved.
Resolution problem: Raisecos window figs

## Slide 6
Wavelet Transform(WT)
Cross correlation
Display the coefficients
Continuous WT: sliding wavelet
Discrete WT: segments (correlate the segments with wavelet at the same time)
How much does the trace resemble the adjusted mother wavelet
Notes: wavelet transform
(CWT) (DWT?)
CWT: sliding window
DWT: window segments (a sequence of windows at the same time)
In my view, wavelet transform is like a cross-correlation between the signal and the adjusted mother wavelet. What we get out of WT is a display of the coefficient of cross-correlation, in other words, the display shows how much alike is the signal compared to adjusted mother wavelet.

## Slide 7
Matching Pursuit(MP)
Cross correlation
Subtract best matched wavelet
Iteration
FT on matched wavelet and project along time
Display
Matching Pursuit: a combination of WT & STFT
Easy reconstruction
Notes: I would say a combination of CWT & STFT regression method
1 cross-correlation
2 Fourier transform
3 project along the window
Instead of using scale we use frequency as the direct parameter here
Easy to reconstruct the signal.
Iteration of CWT
Since the wavelet is axial symmetrical, cross-correlation is the same as convolution between the wavelet and the signal
Greed approach in statistical mean

## Slide 8
Background---STFT, CWT and MPD
Fractional Matching Pursuit Decomposition
Computational Simulation
Results: MPD versus FMPD
Conclusion
Contents

## Slide 9
Fractional MPD
Regression: stability problem
Subtract the matched wavelet with a portion of the coefficient
FMPD: much more laterally stable
Mitigate the interference effect
Notes: I would say a combination of CWT & STFT regression method
1 cross-correlation
2 Fourier transform
3 project along the window
Instead of using scale we use frequency as the direct parameter here
Easy to reconstruct the signal.
Iteration of CWT
Since the wavelet is axial symmetrical, cross-correlation is the same as convolution between the wavelet and the signal
Greed approach in statistical mean

## Slide 10
Background---STFT, CWT and MPD
Fractional Matching Pursuit Decomposition
Computational Simulation
Results: MPD versus FMPD
Conclusion
Contents

## Slide 11
Algorithm
Input seismic trace
Wavelet Dictionary
Wavelet=Ricker(f)
Best Matched Wavelet
Residual
Reconstructed trace
Residual Trace
correlation
subtraction
energy>threshold
energy<threshold
summation
Notes: Different phase = time shifted wave

## Slide 12
Background---STFT, CWT and MPD
Fractional Matching Pursuit Decomposition
Computational Simulation
Results: MPD versus FMPD
Conclusion
Contents

## Slide 13
13

## Slide 14
14

## Slide 16
Ricker Criterion
Rayleigh Criterion

## Slide 17
Ricker Criterion
Rayleigh Criterion

## Slide 21
section 50Hz inline 30 FMPD
section 50Hz inline 30 MPD

## Slide 22
timeslice 34 50Hz MPD

## Slide 23
timeslice 34 50Hz FMPD

## Slide 24
Background---STFT, CWT and MPD
Fractional Matching Pursuit Decomposition
Computational Simulation
Results: MPD versus FMPD
Conclusion
Contents

## Slide 25
Conclusion
Matching Pursuit Decomposition is laterally unstable
Fractional Matching Pursuit Decomposition solves the problem
Notes: More complicate MPD instead of greedy approach could be explored deeper.

## Slide 26
Questions? Comments?
60Hz Ricker
Notes: When we look at the seismic trace, we hope to see bright spot say thank you for getting me out of jail

## Slide 30
30

## Slide 31
31

## Slide 32
Motivation
Alternative time frequency analysis method
New representation provides new perspective new attributes
Convolution model base
Extracted wavelet---Ricker like
Application: Gas Brine differentiation; channel detection
Simple representation---more to discover
Notes: Motivation
An alternative
Gas Brine differentiation
Instead of knowing what frequency occurred at what time. We want to know when did those event occur, those reflection
We tend to simplify complicated seismic trace to convolution model, so what we mostly care is those major events
A new way of representation makes new attributes possible
Instantaneous frequency?